## Slide 1
0
1
2
15
16
MIKUMARI port numbers
TDC 0-31 ch
TDC 32-63 ch
16
*GN-2006-1
*GN-2006-4
SFP1
SFP2
Data link
Not in use
NIM
IN
NIM
OUT
These power supply connectors are connected.
Recommend to put a cover on unused side for your safety.
NIM IN1: Scaler reset
NIM IN2: Trigger (veto) in
NIM OUT1: Heartbeat signal
NIM OUT2: TCP connection
MIKUMARI Clock Primary
0-16: Primary (TX)
LED1: PLL locked
LED2: 0
LED3: Heartbeat frame state
LED4: DAQ is running
DIP1: SiTCP IP setting
DIP2: Not in Use
DIP3: Not in Use
DIP4: Not in Use
＊前のバージョンにあったMIKUMARIの状態を記録するTDCは廃止

## Slide 2
0
1
2
15
16
MIKUMARI port numbers
TDC 0-31 ch
TDC 32-63 ch
16
*GN-2006-1
*GN-2006-4
SFP1
SFP2
Data link
Not in use
NIM
IN
NIM
OUT
These power supply connectors are connected.
Recommend to put a cover on unused side for your safety.
NIM IN1: TDC 64 ch
NIM IN2: Trigger (veto) in
NIM OUT1: Heartbeat signal or Trigger out (from LACCP)
NIM OUT2: TCP connection
MIKUMARI Clock Hub
0-15: Primary (TX)
16: Secondary (RX)
LED1: PLL locked
LED2: MIKUMARI (16) link up
LED3: Ready for DAQ
LED4: DAQ is running
DIP1: SiTCP IP setting
DIP2: Trigger out
DIP3: Not in Use
DIP4: Not in Use
＊前のバージョンにあったMIKUMARIの状態を記録するTDCは廃止

## Slide 3
0
MIKUMARI port numbers
TDC 0-31 ch
TDC 32-63 ch
0
*GN-2006-1
*GN-2006-4
SFP1
SFP2
Data link
Not in use
NIM
IN
NIM
OUT
These power supply connectors are connected.
Recommend to put a cover on unused side for your safety.
NIM IN1: TDC 128 ch
NIM IN2: Trigger in
NIM OUT1: Heartbeat signal or Trigger out (from LACCP)
NIM OUT2: TCP connection
AMANEQ StrLrTdc
0: Secondary (RX)
LED1: PLL locked
LED2: MIKUMARI (0) link up
LED3: Ready for DAQ
LED4: DAQ is running
DIP1: SiTCP IP setting
DIP2: Trigger out
DIP3: Stand alone mode
DIP4: Not in Use
TDC 64-95 ch
TDC 96-127 ch

## Slide 4
今回の運用
MikuClockPrim, MikuClockHub
ParingをOFF。Trailing dataが返ってくる。
AMANEQ StrLrTdc, CIRASAME StrTdc
ParingをON。TOTが入ったleading dataだけ返ってくる。

## Slide 5
0
1
2
15